## Slide 1: The Velocity Mapping Toolbox (VMT): Updates and Applications
OSW Hydroacoustics Webinar
May 20, 2014
Frank Engel
Ryan Jackson
USGS Illinois Water Science Center

## Slide 2: Opening Demo
A quick look at VMT
  Reads TDRI ASCII files (multiple transects)
  Averages to one Mean Cross Section (MCS)
  Quickly allows for robust visualization
[VMT demo outside of presentation]
Notes: Matlab-based ADCP Data Processing and Visualization Code (GUI)
  Most appropriate for data collected with multiple transects at a single cross section and good positional control
Reads ASCII output files from WinRiver II (v4.06 will also read Sontek MAT files)
  GPS required
  Averages multiple transects at a single cross section
Data Processing and Visualization
  Computes a mean velocity field for a given cross section
  Computes velocity components
    Vnorth and Veast, Vstreamwise and VTransverse, & Vprimary and Vsecondary (and vertical)
  Contour plots can be constructed for numerous variables (including backscatter)
    secondary and vertical flow vectors can be overlaid
  Plan view plots show depth- or layer-averaged velocities (for one or more cross sections)
  Additional standalone utilities provide further processing capabilities
Export Capabilities
  Exports data to a variety of formats compatible with Excel®, ArcGIS®, Google Earth®, TecPlot®, and iRIC

## Slide 3: Contributors to VMT
Primary Developers:
Ryan Jackson (USGS Illinois WSC)
*Frank Engel (USGS Illinois WSC)
Dan Parsons (Univ. of Hull, UK)
Jon Czuba (former USGS)
Dave Mueller (USGS OSW)
Input and support from:
Kevin Oberg (USGS OSW)
Bruce Rhoads (University of Illinois)
Kevin Johnson (USGS Illinois WSC)
Jim Best (University of Illinois)
Marcelo Garcia (University of Illinois)
Jim Riley (Eastern Illinois University)
Ricardo Szupiany (Universidad Nacional del Litoral, Argentina)
And many others!
Jackson
Czuba
Parsons
Mueller
Engel
VMT
*Current primary coder

## Slide 4: Timeline
2006
2007
2008
2009
2010
2011
2012
2013
2014
2nd velocity mapping class
1st velocity mapping class
VMT fact sheet
VMT version 4 released
ESPL paper
Mathworks consultation
Snowbird short course
Tampa short course
Santa Fe, Argentina short course
Jackson builds VMT v1
Engel begins contributing
Czuba St. Claire work
Riley confluence work
Parsons & Best Parana work
Basic Matlab codes developed by Dan Parsons
  Transect averaging
  Secondary flow computation
  Site specific
May 2014
Sep 2013
May 2013
May 2013
Oct 2012
Sep 2012
Aug 2012
Mar 2011
Sep 2009
Dec 2008
Aug 2009
Summer 2008
Feb 2007
2006

## Slide 5: Timeline
Feb 2007
2006
2006
2007
2008
2009
2010
2011
2012
2013
2014
2nd velocity mapping class
1st velocity mapping class
VMT fact sheet
VMT version 4 released
ESPL paper
Mathworks consultation
Snowbird short course
Tampa short course
Santa Fe, Argentina short course
Jackson builds VMT v1
Czuba St. Claire work
Riley confluence work
Parsons & Best Parana work
Jon Czuba (USGS) adapts codes for St. Claire River
  TDRI ASCII file parsing
  Basic spatial avg. and visualization
May 2014
Sep 2013
May 2013
May 2013
Oct 2012
Sep 2012
Aug 2012
Mar 2011
Sep 2009
Dec 2008
Summer 2008
Engel begins contributing
Aug 2009

## Slide 6: Timeline
Czuba St. Claire work
Summer 2008
Riley confluence work
Feb 2007
Parsons & Best Parana work
2006
2006
2007
2008
2009
2010
2011
2012
2013
2014
2nd velocity mapping class
May 2014
1st velocity mapping class
Sep 2013
VMT fact sheet
May 2013
VMT version 4 released
May 2013
ESPL paper
Oct 2012
Mathworks consultation
Sep 2012
Snowbird short course
Aug 2012
Tampa short course
Mar 2011
Santa Fe, Argentina short course
Sep 2009
Jackson compiles non-site specific VMT version 1
Engel adds other secondary flow computations, export options, and more
Jackson builds VMT v1
Dec 2008
Engel begins contributing
Aug 2009

## Slide 7: Timeline
Engel begins contributing
Aug 2009
Aug 2012
Mar 2011
Sep 2009
Dec 2008
Summer 2008
Feb 2007
2006
Jackson builds VMT v1
2006
2007
2008
2009
2010
2011
2012
2013
2014
2nd velocity mapping class
1st velocity mapping class
Snowbird short course
Tampa short course
Santa Fe, Argentina short course
Czuba St. Claire work
Riley confluence work
Parsons & Best Parana work
Consultation with Mathworks leads to major redesign (speed, features, workflow enhancement)
Paper on VMT published in ESPL
VMT Fact Sheet
Mathworks consultation
ESPL paper
VMT fact sheet
VMT version 4 released
May 2014
Sep 2013
May 2013
May 2013
Oct 2012
Sep 2012

## Slide 8: Timeline
Engel begins contributing
Aug 2009
May 2013
May 2013
Oct 2012
Sep 2012
Dec 2008
Summer 2008
Feb 2007
2006
Mathworks consultation
ESPL paper
VMT fact sheet
VMT version 4 released
Jackson builds VMT v1
2006
2007
2008
2009
2010
2011
2012
2013
2014
Czuba St. Claire work
Riley confluence work
Parsons & Best Parana work
There have been many short courses on VMT starting in 2009
In 2013, OSW created SW2782 “Velocity Mapping and Bathymetry with ADCPs”
2nd velocity mapping class
1st velocity mapping class
Snowbird short course
Tampa short course
Santa Fe, Argentina short course
May 2014
Sep 2013
Aug 2012
Mar 2011
Sep 2009

## Slide 9: Overview of Basic Workflow
ASCII Files
Configure Parameters
Preprocess
VMT
Plot Shiptracks
Plot Plan View Map
Plot Contour Map
Visualization Engine
Compute Mean Cross Section
Map data to MCS
Interpolate data to grid
Average transects to grid
Compute (u,v,w)
Compute ZSD
Compute Roz
Processing Engine
Save Processed Results
Export Graphics
Export Results
User EPs
Imagery
Shore
line
WinRiverII
Collect ADCP Data
Process & QA/QC
Export ASCII
VMT *.mat File(s)
Various File Types
PNG or JPG
VMT *.mat File
VMT Utilities
ASCII2GIS
ASCII2KML
Similar
Process for
Sontek
(uses MAT file)
Batch Mode
Flat-file Builder
Notes: Green = User set/controlled
Grey = Internal
Yellow = Special

## Slide 10: Averaging Multiple Transects
Data mapped to a mean, linear cross section
(required for secondary flow computations)
If data along a curvilinear path is required, use ASCII2GIS utility
Compute Mean Cross Section
Map data to MCS
Interpolate data to grid
Average transects to grid
Compute (u,v,w)
Compute ZSD
Compute Roz
Processing Engine

## Slide 11: Mean Cross Section
Fits a line to all GPS points
User can override with endpoint file
Compute Mean Cross Section

## Slide 12: Project Data to Mean XS
Map data to MCS

## Slide 13: Interpolate to Uniform Grid
Interpolates data to user
specified grid
X grid node spacing user defined
Z grid node spacing user defined
(TRDI default: ADCP binsize)
Interpolate data to grid

## Slide 14: Average Multiple Transects
Averages basic variables at each node
  Velocity Components (East, North, Vertical, Error)
  Backscatter & Depth
  Velocity magnitude & direction are recomputed from averaged components
Average transects to grid

## Slide 15: Live Demo
VMT allows users to visualize many different variables
Several secondary circulation computation schemes to suite your needs
Variable list continues to grow…
[Demo of VMT outside of presentation]

## Slide 16: Ongoing & future work on VMT
VMT is evolving on a daily basis
VMT already includes additional functionality that is “hidden” including:
  Support for TRDI RiverRay and SonTek data with dynamic bin sizing
  Routines to compute longitudinal dispersion coefficients
  Shear velocity and roughness height based on log-law fits
  Stationary profile analysis tools (STA tool, Boldt)
  Batch processing and custom file builder tools

## Slide 17: Ongoing & future work on VMT
We have recently worked with Mathworks to provide feedback on improvements to the code
The improvements to date will allow future expansion of VMT to be much easier
Expansions currently in development include:
  A suspended sediment concentration calibration and computation plug-in (J. Boldt, KY WSC)
  A GeoViz tool for expanded visualization capabilities (F. Engel, IL WSC)

## Slide 18: Geo-Viz “Teaser”
“GIS-like” interface allowing processing of large multi-transect sites
Survey planning tools
  Transect layout
  Bathymetry interpolation/mapping toolset

## Slide 19: Other future applications & features
Continued efficiency tweaks
Index-Velocity site evaluation toolkit
  Across-channel velocity distribution analysis
  Standard section guidance
Model validation suite
  Output to fixed grid and/or input model results to compare
Survey planning tools
  Transect layout tool and bathymetry interpolation application
GPS.TXT added support (RTK elevations, filtering)
New ideas typically come from YOU—user base feedback is invaluable!!

## Slide 20: User Base
The VMT user base is active and dynamic
  Over 3,100 visitors to the webpage since December 1 2012 from 88 countries
  VMT v4.05 has been downloaded over 1,000 times (EXE and source code)

## Slide 21: Known Applications in North America
VMT is being used outside
of the west and midwest, but we have little feedback
If you have applications of VMT, we want to know about them!
States with trained users
(attended a class)

## Slide 22: Example Applications of VMT
Geomorphology
Morphodynamics of large river meanders
Fluvial dynamics of stream confluences/bifurcations
Sediment transport
Hydrodynamics near Structures
Hydrodynamics near locks and dams and bypass structures
Pier scour
Characterization of flow/bathymetry near channel training structures
Contaminant Transport
Plume tracking
Mixing characterization
Limnology & Nearshore Circulation
Rivermouth hydrodynamics and mixing
Secondary flows in submarine bends
Nearshore circulation
Biological/Ecological Studies
Hydrodynamic requirements for fish spawning
Habitat characterization
Gaging
Evaluation of flow structure and secondary flows at index velocity gages
Locating surface radar gages
Modeling
Collection of model calibration/validation data
Model development (bathymetric mapping)

## Slide 23: Geomorphology
Konsoer, K. M., & Rhoads, B. L. (2011). Spatial–temporal structure of mixing interface turbulence at two large river confluences. Environmental Fluid Mechanics, 1-28.
Wabash-Vermillion Confluence

## Slide 24: Flow and Bathymetry near Structures
ADCP bathymetry
Single beam echo sounder
bathymetry
Data courtesy of E.C Jamieson, C.D Rennie, and R.B. Jacobson
Mississippi River near St. Louis, MO
Missouri River near Columbia, MO
From Jackson (FS 2013-3028)

## Slide 25: Contaminant Transport
Jackson, P.R., Lageman, J.D., 2014, Real-time piscicide tracking using Rhodamine WT dye for support of application, transport, and deactivation strategies in riverine environments: U.S. Geological Survey Scientific Investigations Report 2013–5211, 43 p., http://dx.doi.org/10.3133/sir20135211.
Model results from the Univ. of Illinois
(M.H. Garcia)
ADCP Data
Chicago Sanitary and Ship Canal
Plant Intake
Plant Outfall
Power Plant

## Slide 26: Limnology and Nearshore Circulation
Jackson, P.R., 2013, Circulation, mixing, and transport in nearshore Lake Erie in the vicinity of Villa Angela Beach and Euclid Creek, Cleveland, Ohio, September 11–12, 2012: U.S. Geological Survey Scientific Investigations Report 2013–5198, 34 p., http://dx.doi.org/10.3133/sir20135198.

## Slide 27: Biological Studies
Vs = settling velocity
u* = shear velocity
If u* > Vs, eggs should remain in suspension
Eggs that settle on the bottom are thought to perish
u* ≈ 2.1 cm/s

## Slide 28: Biological Studies
From Murphy and Jackson (SIR 2013-5106)
Murphy, E.A., and Jackson, P.R., 2013, Hydraulic and water-quality data collection for the investigation of Great Lakes tributaries for Asian carp spawning and egg-transport suitability: U.S. Geological Survey Scientific Investigations Report 2013–5106, 30 p., http://pubs.usgs.gov/sir/2013/5106/.
Velocity magnitude
Vertical velocity
Shear velocity
Depth
Temperature
Specific conductance
Dissolved oxygen
pH
Turbidity

## Slide 29: Biological Studies
From Murphy and Jackson (SIR 2013-5106)

## Slide 30: Streamgaging
Jackson, P.R., Johnson, K.K., and Duncker, J.J., 2012, Comparison of index velocity measurements made with a horizontal acoustic Doppler current profiler and a three-path acoustic velocity meter for computation of discharge in the Chicago Sanitary and Ship Canal near Lemont, Illinois: U.S. Geological Survey Scientific Investigations Report 2011–5205, 42 p.

## Slide 31: Model Calibration/Validation
Missouri River near St. Charles, MO
Data collected as part of SW2782 Velocity Mapping and Bathymetry with ADCPs
(modeled in iRIC with FaSTMECH)

## Slide 32: VMT Classes
2009—3 day course (Santa Fe Argentina)
2011—1/2 day short course (Tampa)
2012—1 day short course (HMEM, Utah)
2013, 2014—1 week USGS training course SW2782 Velocity Mapping and Bathymetry with ADCPs (St. Louis)
98 trained
4 agencies (USGS, USACE, USDA, Environment Canada)
25+ academics
7 industry reps
6 countries (US, Canada, Brazil, Belgium, Argentina, Italy)
http://hydroacoustics.usgs.gov/training/register.shtml

## Slide 33: Questions?
Contact Info:
Frank Engel (fengel@usgs.gov); (217) 328-9774
Ryan Jackson (pjackson@usgs.gov); (217) 328-9719
VMT Webpage:
http://hydroacoustics.usgs.gov/movingboat/VMT/VMT.shtml

## Slide 34: Additional Information

## Slide 35: An Incomplete List of Application Sites
1 Congo River (DRC, Africa)
2 Mississippi River (IL, MO, LA, MS)
3 Missouri River (MO)
4 Ohio River (IL, KY)
5 Chicago Sanitary and Ship Canal (IL)
6 Chicago Lakefront (Lake Michigan) (IL)
7 Lake Erie at Villa Angela Beach (OH)
8 Milwaukee River (WI)
9 Menomonee River (WI)
10 Kinnickinnic River (WI)
11 Green Bay (WI)
12 Manitowoc River (WI)
13 Sandusky River (OH)
14 Maumee River (OH)
15 Clinton Lake (IL)
16 Wonder Lake (IL)
17 Wabash River (IL, IN)
18 Embarras River (IL)
19 Hurunui River (New Zealand)
20 Clutha River (New Zealand)
21 Vermillion River (IL)
22 Boise River (ID)
23 Kootenai River (ID)
24 White River (IN)
25 Cal-Sag Channel (IL)
26 Lake Calumet (IL)
27 Yellow Sea (China)
28 Yellow River (China)
29 Parana River (Argentina)
30 Rio Coronda (Argentina)
31 Madeira River (Brazil)
32 Fox River (IL)
33 Arkansas River (AR)
34 Cowlitz River (WA)
35 Umqua River (OR)
36 St. Lawrence River (Canada)
37 Des Plaines River (IL)
38 Illinois River (IL)
39 Little Calumet River (IL)
40 Fraser River (BC, Canada)
41 St. Clair River (MI, Canada)
42 Big Muddy Creek (IL)
43 Little Wabash River (IL)
44 Yuma Canal (AZ)
45 Sacramento River (CA)
46 New Castle Reservoir (UT)
47 St. Marys River (MI, Canada)
48 Jordan River (UT)
49 All American Canal (AZ)
50 Coachella Canal (AZ)
51 Sangamon River (IL)
52 Columbia River (WA, OR)
53 Snake River (WA)
54 Shepaug River (CT)
55 Susquehanna River (CT)
56 Lake Lillinonah (CT)
57 Patoka Lake (KY)
58 Rasmussen Lake (IL)
59 Colastine River (Argentina)
60 Fire Island Breach (NY)
61 Sugar Creek (IL)

## Slide 36: Known Projects Using/Citing VMT

## Slide 37: Projects Citing VMT Continued